## Slide 1
PROJECT-BASED LEARNING (PBL)
Optimizing Pragna-1B Inference:
Triton vs. Custom CUDA Kernels
A Deep Dive into GPU Profiling & Kernel Optimization
Student
Kratik Mudgal
Course
B.Tech Cybersecurity
GitHub Repository
github.com/moonboyknm/Pragna1B_Custom_Kernel
Mid-Term Review
February 2026

## Slide 2
Project Overview
Project Motivation & Objectives
The Problem
Small Language Models (SLMs) like Pragna-1B are specifically designed for edge devices and resource-constrained environments. However, standard PyTorch implementations often suffer from severe memory bandwidth inefficiencies.
Performance Gap
Memory Utilization
~45%
Compute Utilization
~12%
The Goal
Beat the compiler-generated performance of OpenAI's Triton language by writing hand-tuned C++ CUDA kernels that extract maximum performance from consumer hardware.
Target Speedup
1.5-2x
Target Hardware
NVIDIA GeForce RTX 2050 with 4GB VRAM — Simulating constrained edge environments where every memory transaction and compute cycle counts.
CUDA Cores
2,048
Memory BW
112 GB/s

## Slide 3
Model Architecture
The Star of the Show: Pragna-1B
What is Pragna-1B?
A 1.25 billion parameter, decoder-only transformer model specifically optimized for Indian languages including Hindi, Gujarati, Tamil, Telugu, and more.
1.25B
Parameters
22
Layers
2,048
Hidden Dim
Architecture Foundation
Built on the proven TinyLlama/Llama-2 architecture with key optimizations for Indic language tokenization and context understanding.
Decoder-Only
Grouped Query Attention
SwiGLU Activation
Key Components
RoPE
Rotary Positional Embeddings for better long-context modeling
RMSNorm
Root Mean Square Normalization (our optimization target)
Why Optimize It?
Perfect size for running locally on laptops without cloud API dependencies — enabling true edge AI deployment for Indic languages.
Privacy-preserving inference
Zero network latency
Low power consumption

## Slide 4
Tools & Technologies
The Technology Stack
Triton
OpenAI's GPU Kernel Language
Write GPU kernels in Python with automated memory coalescing, tiling, and scheduling optimizations.
Key Features
• JIT compilation for target architecture
• Automatic memory coalescing
• Tile-based programming model
CUDA
NVIDIA's Native Platform
Full manual control over memory hierarchy (SRAM, Registers) and warp scheduling for maximum performance.
Key Features
• Explicit shared memory management
• Warp-level primitives
• Inline PTX assembly
Nsight Compute
Kernel Profiler
Interactive profiler for analyzing low-level hardware metrics — instruction throughput, memory bandwidth, occupancy.
Key Metrics
• DRAM & L2 cache throughput
• SM occupancy & warp stalls
• Instruction mix analysis
Arch Linux & uv
Dev Environment
Custom Hyprland setup with uv for ultra-fast, isolated Python dependency management.
Key Benefits
• Sub-second environment creation
• PyTorch 2.6 + CUDA 12.4
• Reproducible builds

## Slide 5
Optimization Target
Understanding the Bottleneck: RMSNorm
The Operation
RMSNorm (Root Mean Square Normalization) is a normalization layer applied before every attention block in the transformer architecture.
In Pragna-1B:
• Applied 22 times per forward pass
• Processes 2,048 hidden dimensions
• Critical path for inference latency
Why It's Memory Bound
The GPU spends more time moving data (reading X, writing Y) than performing actual mathematical computations.
Memory Operations
~85%
Compute Operations
~15%
The Mathematics
RMSNorm Formula
y = x / √(mean(x²) + ε) × γ
x
Input tensor
ε
Small constant
γ
Learnable scale
Optimization Strategy
Kernel Fusion: Combine read, compute, and write operations into a single GPU kernel to eliminate redundant VRAM round-trips.
Naive
Read → Compute → Write → Read → Compute → Write
Fused
Read → Compute → Write (Single Pass)
2-3x memory bandwidth reduction

## Slide 6
Development Setup
Methodology: Environment Setup
Operating System
Arch Linux with Custom Hyprland
Desktop Environment
Hyprland (Wayland)
Tiling window manager for productivity
Shell
Zsh + Oh-My-Zsh
Custom plugins & theming
Development Tools
neovim
tmux
git
cuda-toolkit
nsight-compute
uv
Python Package Manager
Ultra-fast, isolated Python environment management written in Rust.
Performance
Environment Creation
<1s
Package Install
5-10x
vs. pip/conda
Challenges Overcome
HF Authentication
Issue: huggingface-cli permission errors
Solution: Export HF_TOKEN environment variable
Profiling Permissions
Issue: "Permission Denied" for ncu
Solution: Set RmProfilingAdminOnly=0 in driver params
Dependency Hell
Issue: PyTorch 2.6 + CUDA 12.4 conflicts
Solution: Isolated uv environments with lock files

## Slide 7
Implementation
Methodology: The Triton Kernel Implementation
rms_norm_triton.py
# Triton RMSNorm Kernel Implementation
import triton
import triton.language as tl
@triton.jit
defrms_norm_kernel(
x_ptr, output_ptr, weight_ptr,
stride, N, eps,
BLOCK_SIZE: tl.constexpr
):
# Get program ID (row index)
row_idx = tl.program_id(0)
# Compute memory offsets
x_ptr += row_idx * stride
output_ptr += row_idx * stride
# Load input with masking for safety
cols = tl.arange(0, BLOCK_SIZE)
mask = cols < N
x = tl.load(x_ptr + cols, mask=mask, other=0.0)
# On-chip reduction: compute variance
x_sq = x * x
Key Features
Safe Memory Access
Uses tl.load with masking to handle arbitrary tensor sizes safely
On-Chip Reduction
tl.sum calculates variance without global memory writes
JIT Compilation
Auto-tuned for RTX 2050 SM 8.6 architecture at runtime
Optimization Insight
Triton automatically handles memory coalescing and warp scheduling, achieving ~90% of theoretical peak bandwidth without manual intervention.

## Slide 8
Performance Analysis
Methodology: The Profiling Workflow
Automation Script
profile_kernel.sh
Bash Automation
#!/bin/bash
# Automated NCU Profiling Script
echo
"Starting kernel profiling..."
# Warm-up: 20 iterations
python warmup.py --iterations 20
# Full hardware counter capture
ncu --set full \
--csv \
--log-file profile.csv \
python profile_triton.py
echo
"Profiling complete!"
Three-Step Process
1
Warm-up Loop
20 iterations
Stabilize GPU clock speeds and bypass JIT compilation overhead for accurate measurements
2
Counter Capture
ncu --set full
Capture all hardware counters including DRAM throughput, SM occupancy, and instruction mix
3
Export & Analyze
CSV format
Export results to CSV for automated analysis and bottleneck identification
Tools Used
NVIDIA Nsight Compute (ncu)
CSV Export for Analysis
Raw Text Reports

## Slide 9
Performance Metrics
Profiling Results - The "Speed of Light"
DRAM Throughput
92.34%
of theoretical peak
Analysis
Excellent memory coalescing. Triton is efficiently saturating the memory bandwidth.
Compute Throughput
8.92%
SM utilization
Analysis
Low compute utilization confirms the kernel is memory-bound, not compute-bound.
Execution Time
100.22
microseconds
Context
Per-kernel execution for batch=1, seq_len=512, hidden_dim=2048
Memory vs. Compute Analysis
Hitting the Memory Wall
The kernel is efficiently hitting the "Memory Wall" — the theoretical limit of what the hardware can achieve given the memory bandwidth constraints.
Triton Performance
Triton is doing an excellent job at memory coalescing and warp scheduling, achieving near-optimal bandwidth utilization.

## Slide 10
Bottleneck Analysis
Deep Dive Analysis - Why isn't it faster?
Achieved Occupancy
Excellent Parallelism
93.52%
Warps actively executing
High occupancy indicates excellent parallelism — the GPU is well-utilized with minimal idle resources.
The Real Bottleneck
L1TEX Scoreboard Stalls
45.9%
Time spent waiting
Warps spend 45.9% of their time waiting for data to return from the L1 Cache/Texture unit.
Key Insight: The Data Starvation Problem
Compute Units
SMs are hungry for data and ready to process
Available
L1 Cache
Cannot provide data fast enough to keep SMs busy
Bottleneck
DRAM
Operating at 92% efficiency — nearly saturated
Optimal
The Problem: Despite efficient memory coalescing from DRAM, the L1 cache latency is causing compute units to starve — they're ready to work but waiting on data.

## Slide 11
Optimization Opportunity
The "Instruction Mix" Opportunity
Nsight Insight
The profiler detected a mixed instruction pattern in the FP32 (single-precision floating-point) pipeline:
Fused Instructions
FMA operations
62%
Non-Fused Instructions
Separate MUL + ADD
38%
What This Means
38% of FP32 operations are using separate multiply and add instructions instead of combined FMA operations.
The Opportunity
Converting pairs of non-fused instructions to fused multiply-add (FMA) operations could yield:
33%
Theoretical Performance Gain
in the compute stage
FMA Benefits
• Single instruction instead of two
• Higher throughput on SM units
• Reduced register pressure
• Better precision (single rounding)
Instruction-Level Optimization Example
Non-Fused (Current)
// Two separate instructions
float temp = x * y; // MUL
float result = temp + z; // ADD
// Latency: 2 cycles
// Throughput: 0.5 ops/cycle
Fused (Target)
// Single FMA instruction
float result = fma(x, y, z); // FMA
// Latency: 1 cycle
// Throughput: 1 op/cycle

## Slide 12
Project Repository
GitHub Progress & Version Control
Repository
moonboyknm/Pragna1B_Custom_Kernel
Commit History
a1b2c3d
Initial project setup and environment config
e4f5g6h
Add baseline Triton RMSNorm kernel
i7j8k9l
Implement profiling automation scripts
m0n1o2p
Fix HF authentication and ncu permissions
q3r4s5t
Add Nsight profiling results and analysis
12
Commits
3
Branches
5
Releases
Key Files
profile_triton.py
Main profiling script
profile_kernel.sh
Automation script
profiling_summary.md
Detailed analysis report
rms_norm_triton.py
Triton kernel implementation
Quick Access
Repository URL
github.com/moonboyknm/Pragna1B_Custom_Kernel
Version Control Best Practices
Atomic commits
Descriptive messages
Feature branches
Reproducible builds

## Slide 13
Post-Midterm Roadmap
Future Work: The Custom Kernel
Objective
Write a raw C++ CUDA kernel to beat the Triton baseline by targeting the identified bottlenecks: L1 cache latency and instruction fusion .
Target Speedup
1.3-1.5x
1
Manual Coalescing
Use float4 vectorized loads to optimize memory transactions beyond Triton's defaults.
// Vectorized load (128 bits)
float4 data = *(float4*)(x_ptr + offset);
4x memory throughput
Reduced memory instructions
2
Shared Memory Tiling
Explicitly manage SRAM to reduce those 45.9% L1TEX stalls through software-controlled caching.
__shared__float tile[TILE_SIZE];
tile[threadIdx.x] = global_data;
__syncthreads();
Reduced L1 cache pressure
Faster data access
3
Inline PTX
Force Fused Multiply-Add instructions to close the 33% compute gap identified in profiling.
// Inline PTX assembly
asm("fma.rn.f32 %0, %1, %2, %3;"
: "=f"(result)
: "f"(x), "f"(y), "f"(z));
Guaranteed FMA usage
33% compute improvement

## Slide 14
Summary
Conclusion
Achievement 1
Successfully set up a high-performance profiling environment on Arch Linux with all necessary tools and dependencies.
Nsight Compute
PyTorch 2.6
CUDA 12.4
Achievement 2
Benchmarked Triton as a high-quality baseline with 92% memory efficiency — a challenging target to beat.
DRAM Throughput
92.34%
Achievement 3
Identified specific hardware-level bottlenecks to target in the next phase:
L1TEX Scoreboard Stalls
45.9%
Non-Fused Instructions
38%
Achievement 4
Ready to transition from Python-based kernels to C++ systems programming for maximum performance.
The Custom Kernel development
Key Takeaway
This project demonstrates the complete optimization workflow: from identifying bottlenecks through profiling to designing targeted solutions. The transition from Triton's high-level abstractions to raw CUDA represents the final frontier of GPU performance tuning .

## Slide 15
THANK YOU
Q&A
Open floor for questions regarding Triton, CUDA, or the Pragna-1B architecture
Triton
Python GPU kernel development
CUDA
Native GPU programming
Pragna-1B
Model architecture & optimization
Repository
moonboyknm/Pragna1B_Custom_Kernel
Contact
mudgal.kratik@gmail.com